## Slide 1: Unit OS6: Device Management
6.1. Principles of I/O Systems

## Slide 2: Copyright Notice © 2000-2005 David A. Solomon and Mark Russinovich
These materials are part of the Windows Operating System Internals Curriculum Development Kit, developed by David A. Solomon and Mark E. Russinovich with Andreas Polze
Microsoft has licensed these materials from David Solomon Expert Seminars, Inc. for distribution to academic organizations solely for use in academic environments (and not for commercial use)

## Slide 3: Roadmap for Section 6.1
Principles of I/O Hardware
Structuring of I/O Software
Layers of an I/O System
Operation of an I/O System
Notes: The control of devices connected to a computer is a major objective of any operating system. The I/O subsystem of an OS kernel implements a variety of methods to control all the different devices attached to today’s computers. The I/O subsystem helps to isolate applications and the rest of the kernel from the complexity of managing I/O devices.
The basic I/O hardware elements, such as ports, buses, and device controllers accommodate a wide variety of I/O devices. The OS kernel uses the concept of device derivers to encapsulate implementation details of the different devices. In addition, device drivers provide a uniform interface to the I/O subsystem. In turn, the I/O system’s functionality is exported to applications through a standard system call interface (I.e.; Windows API, Posix API).

## Slide 4: Input/Output – Principles of I/O Hardware
Major components of a computer system: CPU, memories (primary/secondary), I/O system
I/O devices:
  Block devices – store information in fixed-sized blocks; typical sizes: 128-1024 bytes
  Character devices – delivers/accepts stream of characters
Device controllers:
  Connects physical device to system bus (Minicomputers, PCs)
  Mainframes use a more complex model: Multiple buses and specialized I/O computers (I/O channels)
Communication:
  Memory-mapped I/O, controller registers
  Direct Memory Access - DMA
Notes: <number>
<footer>
<header>
<date/time>
A general-purpose computer system consists of a CPU and a number of device controllers that are connected through a common bus. Each device controller is in charge of a specific type of device. Depending on the controller, there may be more than one device attached to it. For instance the SCSI (Small Computer Systems Interface) controller can have as many as seven devices attached to it.
A device controller maintains some local buffer storage and a set of special-purpose registers. The controller is responsible for moving data between the peripheral device(s) it controls and its local buffer storage. The size of the local buffer within the device controller varies from one controller to another, depending on the particular device being controlled.

## Slide 5: I/O Hardware - Single Bus
CPU
Memory
Video Controller
Keyboard Controller
Floppy Controller
Disk Controller
System bus
Monitor
Keyboard
Floppy drive
Disk drive
Notes: <number>
<footer>
<header>
<date/time>
The logical structure of a simple low-end personal computer is centered around a single bus, which is used to connect the CPU, memory, and I/O devices. Each I/O device consists of two parts: one containing most of the electronics, called the controller, and one containing the I/O device itself, such as a disk drive. The controller is usually contained on a board plugged into a free slot of the motherboards, except for those controllers that are not optional (e.g.; the keyboard), which are sometimes located on the motherboard.

## Slide 6: I/O Hardware - Multiple Buses
Video controller
Network controller
IDE disk controller
USB interface
keyboard
mouse
CPU
PCI bridge/ memory controller
Memory
Cache
SCSI controller
SCSI disk
SCSI disk
SCSI disk
PCI bus
USB bus
SCSI bus
Memory bus
Notes: <number>
<footer>
<header>
<date/time>
Most modern PCs are centered around the PCI (Peripheral Component Interconnect) bus and use more than one bus. We have depicted a configuration in which the CPU talks to the memory over a dedicated high-speed connection. The PCI controller talks to the memory and to the PCI bus directly, so CPU-memory traffic does not go over the PCI bus. High-bandwidth peripherals (SCSI disks) can connect to the PCI bus directly. In addition, the PCI bus has a bridge to the ISA (Industry Standard Architecture) bus, so that ISA controller and their devices can still be used.

## Slide 7: Diversity among I/O Devices
The I/O subsystem has to consider device characteristics:
Data rate:
  may vary by several orders of magnitude
Complexity of control:
  exclusive vs. shared devices
Unit of transfer:
  stream of bytes vs. block-I/O
Data representations:
  character encoding, error codes, parity conventions
Error conditions:
  consequences, range of responses
Applications:
  impact on resource scheduling, buffering schemes

## Slide 8: Organization of the I/O Function
Programmed I/O with polling:
  The processor issues an I/O command on behalf of a process
  The process busy waits for completion of the operation before proceeding
Interrupt-driven I/O:
  The processor issues an I/O command and continues to execute
  The I/O module interrupts the processor when it has finished I/O
  The initiator process may be suspended pending the interrupt
Direct memory access (DMA):
  A DMA module controls exchange of data between I/O module and main memory
  The processor requests transfer of a block of data from DMA and is interrupted only after the entire block has been transferred

## Slide 9: Flow of a blocking I/O request
Thread issues blocking read() system call
Kernel checks parameters; may return buffered data and finish
Thread is removed from run queue if physical I/O required; added to wait queue for device; I/O request is scheduled
Device driver allocates kernel buffer; sends command to controller
Device controller operates the hardware to perform data transfer
Driver may poll for status and data; or set up DMA that will generate interrupt
Interrupt occurs; handler stores data; signals device driver
Device driver receives signal; determines request status; signals kernel I/O subsystem
Kernel transfers data or return code to user space; removes thread from wait queue
Thread resumes execution at completion of read() call

## Slide 10: Principles of I/O Software
Layered organization
Device independence
Error handling
  Error should be handled as close to the hardware as possible
  Transparent error recovery at low level
Synchronous vs. Asynchronous transfers
  Most physical I/O is asynchronous
  Kernel may provide synchronous I/O system calls
Sharable vs. dedicated devices
  Disk vs. printer
Structuring of
I/O software
User-level software
Device-independent OS software
Device drivers
Interrupt handlers
Notes: <number>
<footer>
<header>
<date/time>
Modern operating systems are interrupt driven. If there are no processes to execute, no I/O devices to service, and no users to whom to respond, an operating system will sit quietly, waiting for something to happen. Events are almost always signaled by occurrence of an interrupt, or a trap.
When an interrupt occurs, the hardware transfers control to the operating system. First, the operating system preserves the state of the CPU by storing registers and the program counters. Then, it determines which type of interrupt has occurred. This determination may require polling, the querying of all I/O devices to detect which requested service, or it may be a natural result of a vectored interrupt system.
To start an I/O operation, the CPU loads the appropriate registers within the device controller. The device controller, in turn, examines the contents of these registers to determine which action to take. For example, if it finds a read request, the controller will start the transfer of data from the device to its local buffer. Once the transfer of data is complete, the device controller informs the CPU that it has finished its operation. It accomplishes this communication by causing an interrupt.

## Slide 11: Interrupt Handlers
Should be hidden by the operating system
Every thread starting an I/O operation should block until I/O has completed and interrupt occurs
Interrupt handler transfers data from device (controller) and un-blocks process

## Slide 12: Device Driver
Contains all device-dependent code
Handles one device
Translates abstract requests into device commands
  Writes controller registers
  Accesses mapped memory
  Queues requests
Driver may block after issuing a request:
  Interrupt will un-block driver (returning status information)

## Slide 13: Device-independent I/O Software
Functions of device-independent I/O software:
Uniform interfacing for the device drivers
Device naming
Device protection
Providing a device-independent block size
Buffering
Storage allocation on block devices
Allocating and releasing dedicated devices
Error reporting

## Slide 14: Layers of the I/O System
User-Space I/O Software
System call libraries (read, write,...)
Spooling
  Managing dedicated I/O devices in a multiprogramming system
  Daemon process, spooling directory
  lpd – line printer daemon, sendmail – simple mail transfer protocol
Layer
User process
Device-independent software
Device drivers
Interrupt handlers
Hardware
I/O request
I/O reply
I/O functions
I/O calls, spooling format I/O
Naming, protection buffering, blocking
Setup registers,
Check status
Setup registers,
Check status
Wakeup driver
Perform I/O op.

## Slide 15: Application I/O Interfaces
The OS system call interface distinguished device classes:
Character-stream or block
Sequential or random-access
Synchronous or asynchronous
Sharable or dedicated
Speed of operation
Read/write, read only, write only

## Slide 16: Example: 4.3 BSD kernel I/O structure
The hardware
socket
Plain file
protocols
File system
Cooked block interface
Raw block interface
Raw tty interface
cooked TTY
Line discipline
Network interface
Block-device driver
character-device driver
System-call interface to the kernel

## Slide 17: Further Reading
Abraham Silberschatz, Peter B. Galvin, Operating System Concepts, John Wiley & Sons, 6th Ed., 2003;
  Chapter 2 - Computer-System Structures
  Chapter 13 - I/O Systems