## Slide 1: Unit OS9: Real-Time and Embedded Systems
9.2. Real-Time Systems with Windows

## Slide 2: Copyright Notice © 2000-2005 David A. Solomon and Mark Russinovich
These materials are part of the Windows Operating System Internals Curriculum Development Kit, developed by David A. Solomon and Mark E. Russinovich with Andreas Polze
Microsoft has licensed these materials from David Solomon Expert Seminars, Inc. for distribution to academic organizations solely for use in academic environments (and not for commercial use)

## Slide 3: Roadmap for Section 9.2
Windows NT/2000/XP/2003 real-time behavior
Windows NT/2000/XP/2003 I/O system and interrupt handling revisited
Windows CE - a contrasting approach
Windows CE scheduling
Windows CE interrupt architecture
Deterministic real-time systems with Windows CE
Notes: Although many types of embedded systems (for example, printers and automotive computers) have real-time requirements, Windows XP Embedded doesn’t have real-time characteristics. It is simply a version of Windows XP that makes it possible, to produce small-footprint versions of Windows XP suitable for running on devices with limited resources.
Because Windows XP doesn’t prioritize device IRQs in any controllable way and user-level applications execute only when a processor’s IRQL is at passive level, Windows isn’t always suitable as a real-time operating system. The system’s devices and device drivers—not Windows—ultimately determine the worst-case delay.
In contrast, Windows CE offers some real-time capabilities. In particular, Windows CE is providing:
Guaranteed upper bounds on high-priority thread scheduling—only for the highest-priority thread among all the scheduled threads.
Guaranteed upper bound on delay in scheduling high-priority interrupt service routines (ISRs). The kernel has a few places where pre-emption is turned off for a short, bounded time.
Fine control over the scheduler and how it schedules threads.
This section will briefly describe the Windows CE approach to real time and scheduling and compare it with Windows XP.

## Slide 4: Definition of a Real-Time System
From comp.realtime:
"A real-time system is one in which the correctness of the computations not only depends on the logical correctness of the computation, but also on the time at which the result is produced. If the timing constraints of the system are not met, system failure is said to have occurred.“
The RT OS is just one element of the complete real-time system and must provide sufficient functionality to enable the overall real-time system to meet its requirements.
  Distinguish between a fast operating system and an RTOS
Notes: <number>
<footer>
<header>
<date/time>
In addition, the OS behavior must be predictable. This means real-time system developers must have detailed information about the system interrupt levels, system calls, and timing:
  The maximum time during which interrupts are masked by the OS and by device drivers must be known.
  The maximum time that device drivers use to process an interrupt, and specific IRQ information relating to those device drivers, must be known.
  The interrupt latency (the time from interrupt to task run) must be predictable and compatible with application requirements.
The time for every system call should be predictable and independent of the number of objects in the system. This paper describes how Microsoft Windows CE operating system meets each of these requirements for a real-time operating system. Most significant, Windows CE guarantees an upper bound on the time it takes to start a real-time priority thread after receiving an interrupt.

## Slide 5: Requirements for a RT OS
The OS (operating system) must be multithreaded and preemptive
The OS must support thread priority
A system of priority inheritance must exist
The OS must support predictable thread synchronization mechanisms
In addition, the OS behavior must be predictable. This means real-time system developers must have detailed information about the system interrupt levels, system calls, and timing:
  The maximum time during which interrupts are masked by the OS and by device drivers must be known.
  The maximum time that device drivers use to process an interrupt, and specific IRQ information relating to those device drivers, must be known.
  The interrupt latency (the time from interrupt to task run) must be predictable and compatible with application requirements.

## Slide 6: Windows: Thread Priority Levels
16 “real-time” levels
15 variable levels
Used by zero page thread
Used by idle thread(s)
31
16
0
i
15
1
Even real-time threads have no guaranteed timing behavior
  Windows scheduler is interrupted by I/O activities (ISR, DPC, APC)
  Device drivers heavily impact Windows timing behavior
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Windows Real-Time Threads
Real-time threads are special:
Priorities in real-time range never get boosted
  Priorities stay fixed relative to other real-time threads

## Slide 8: Thread Scheduling Priorities vs. Interrupt Request Levels (IRQLs)
Passive_Level
APC
Dispatch/DPC
Device 1
.
.
.
Device n
Clock
Interprocessor Interrupt
Power fail
High
Hardware
interrupts
IRQLs (x86)
Software
interrupts
0
1
2
30
29
28
31
Thread priorities
0-31
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Interrupt Levels vs. Priority Levels (discussion contd.)
Threads normally run at IRQL 0 or 1
User-mode threads always run at IRQL 0
  No user-mode thread, regardless of its priority, blocks hardware interrupts
  Although high-priority real-time threads can block the execution of important system threads
Only kernel-mode APCs execute at IRQL 1
  They interrupt the execution of a thread
  Threads running in kernel mode can raise IRQL to higher levels, though— for example, while executing a system call that involves thread dispatching
Notes: IRQL - Interrupt Request Level
APC - Asynchronous Procedure Call
DPC - Deferred Procedure Call

## Slide 10: Windows Real-Time Behavior: I/O system and interrupt processing revisited
Windows doesn’t prioritize device interrupts in any controllable way
  User-level applications execute only when a processor’s IRQL is at passive level
  Starvation priority boost for threads may circumvent priority inversion - but without predicable timing behavior
Devices and device drivers determine the worst-case response time
  Sum of all the delays a system’s DPCs and ISRs introduce usually far exceeds the tolerance of a time-sensitive system
-> Let us revisit the Windows I/O system and interrupt handling mechanisms

## Slide 11: Driver Object
A driver object represents a loaded driver
  Names are visible in the Object Manager namespace under \Drivers
  A driver fills in its driver object with pointers to its I/O functions e.g. open, read, write
  When you get the “One or More Drivers Failed to Start” message its because the Service Control Manager didn’t find one or more driver objects in the \Drivers directory for drivers that should have started

## Slide 12: Device Objects
A device object represents an instance of a device
  Device objects are linked in a list off the driver object
  A driver creates device objects to represent the interface to the logical device, so each generally has a unique name visible under \Devices
  Device objects point back at the Driver object

## Slide 13: Driver and Device Objects
\TCPIP
Driver Object
\Device\TCP
\Device\UDP
\Device\IP
Dispatch Table
Open
Write
Read
Loaded Driver Image
Open(…)
Read(…)
Write(…)
TCP/IP Drivers Driver and Device Objects

## Slide 14: File Objects
Represents open instance of a device (files on a volume are virtual devices)
  Applications and drivers “open” devices by name
  The name is parsed by the Object Manager
  When an open succeeds the object manager creates a file object to represent the open instance of the device and a file handle in the process handle table
A file object links to the device object of the “device” which is opened
File objects store additional information
  File offset for sequential access
  File open characteristics (e.g. delete-on-close)
  File name
  Accesses granted for convenience

## Slide 15: I/O Request Packets
System services and drivers allocate I/O request packets to describe I/O
IRP consists of two parts:
  Fixed portion (header):
    Type and size of the request
    Whether request is synchronous or asynchronous
    Pointer to buffer for buffered I/O
    State information (changes with progress of the request)
  One or more stack locations:
    Function code
    Function-specific parameters
    Pointer to caller‘s file object
The I/O Manager locates the driver to which to hand the IRP by following the links:
File Object
Device Object
Driver Object

## Slide 16: Flow of an I/O Request
Environment subsystem or DLL
Services
I/O manager
IRP header
WRITE
parameters
File object
Device object
Driver object
IRP stack location
Dispatch routine(s)
Start I/O
ISR
DPC routine
Device Driver
An application writes a file to the printer, passing a handle to the file object
2)The I/O manager creates an IRP and initializes first stack location
3)The I/O manager uses the driver object to locate the WRITE dispatch routine and calls it, passing the IRP
User mode
Kernel mode
Notes: <number>
<footer>
<header>
<date/time>
The I/O request packet (IRP) is where the I/O system stores information it needs to process an I/O request. When a thread calls an I/O service, the I/O manager constructs an IRP to represent the operation as it progresses through the I/O system. If possible, the I/O manager allocates IRPs from one of two per-processor IRP nonpaged look-aside lists: the small-IRP look-aside list stores IRPs with one stack location, and the large-IRP look aside lists contains IRPs with eight stack locations.
If an IRP requires more than eight stack locations, the I/O manager allocates IRPs from nonpaged pool. After allocation and initializing an IRP, the I/O manager stores a pointer to the caller‘s file object in the IRP.

## Slide 17: I/O Processing – synch. I/O to a single-layered driver
The I/O request passes through a subsystem DLL
The subsystem DLL calls the I/O manager‘s NtWriteFile() service
I/O manager sends the request in form of an IRP to the driver (a device driver)
The driver starts the I/O operation
When the device completes the operation and interrupts the CPU, the device driver services the interrupt
The I/O manager completes the I/O request

## Slide 18: Completing an I/O request
Servicing an interrupt:
  ISR schedules Deferred Procedure Call (DPC); dismisses int.
  DPC routine starts next I/O request and completes interrupt servicing
  May call completion routine of higher-level driver
I/O completion:
  Record the outcome of the operation in an I/O status block
  Return data to the calling thread – by queuing a kernel-mode Asynchronous Procedure Call (APC)
  APC executes in context of calling thread; copies data; frees IRP; sets calling thread to signaled state
  I/O is now considered complete; waiting threads are released

## Slide 19: Flow of Interrupts
Peripheral Device Controller
CPU Interrupt Controller
CPU Interrupt Service Table
0
2
3
n
ISR Address
Spin Lock
Dispatch Code
Interrupt Object
Read from device
Acknowledge-Interrupt
Request DPC
Driver ISR
Raise IRQL
Lower IRQL
KiInterruptDispatch
Grab Spinlock
Drop Spinlock
Notes: EXPERIMENT: Examining Interrupt Internals
Using the kernel debugger, you can view details of an interrupt object, including its IRQL, ISR address, and custom interrupt dispatching code. First, execute the !idt –a command (you may first have to type .reload nt to load kernel symbols) and locate the entry that includes a reference to I8042KeyboardInterruptService, the ISR routine for the PS2 keyboard device:
31: 8a39dc3ci8042prt!I8042KeyboardInterruptService(KINTERRUPT 8a39dc00)
To view the contents of the interrupt object associated with the interrupt, execute dt nt!_kinterrupt with the address following KINTERRUPT:
kd> dt nt!_kinterrupt 8a39dc00
nt!_KINTERRUPT +0x000Type : 22 +0x002Size : 484 +0x004InterruptListEntry :_LIST_ENTRY [0x8a39dc04- 0x8a39dc04 ] +0x00cServiceRoutine : 0xba7e74a2 i8042prt!I8042KeyboardInterruptService+0 +0x010ServiceContext : 0x8a067898 +0x014SpinLock : 0 +0x018TickCount : 0xffffffff +0x01cActualLock : 0x8a067958 -> 0 +0x020DispatchAddress : 0x80531140 nt!KiInterruptDispatch+0 +0x024Vector : 0x31 +0x028Irql : 0x1a’’ +0x029SynchronizeIrql : 0x1a’’ +0x02aFloatingSave : 0’’ …
In this example, the IRQL Windows assigned to the interrupt is 0x1a (which is 26 in decimal). Because this output is from a uniprocessor x86 system, we calculate that the IRQ is 1, because IRQLs on x86 uniprocessors are calculated by subtracting the IRQ from 27. We can verify this by opening the Device Manager, locating the PS/2 keyboard device, and viewing its resource assignments.

## Slide 20: Servicing an Interrupt: Deferred Procedure Calls (DPCs)
Used to defer processing from higher (device) interrupt level to a lower (dispatch) level
  Also used for quantum end and timer expiration
Driver (usually ISR) queues request
  One queue per CPU. DPCs are normally queued to the current processor, but can be targeted to other CPUs
  Executes specified procedure at dispatch IRQL (or “dispatch level”, also “DPC level”) when all higher-IRQL work (interrupts) completed
  Maximum times recommended: ISR: 10 usec, DPC: 25 usec
    See http://www.microsoft.com/whdc/driver/perform/mmdrv.mspx
queue head
DPC object
DPC object
DPC object
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Delivering a DPC
DPC
DPC routines can call kernel functions but can‘t call system services, generate page faults, or create or wait on objects
DPC routines can‘t assume what process address space is currently mapped
Interrupt dispatch table
high
Power failure
Dispatch/DPC
APC
Low
DPC
1. Timer expires, kernel queues DPC that will release all waiting threads Kernel requests SW int.
DPC
DPC
DPC queue
2. DPC interrupt occurs when IRQL drops below dispatch/DPC level
dispatcher
3. After DPC interrupt, control transfers to thread dispatcher
4. Dispatcher executes each DPC routine in DPC queue
Notes: <number>
<footer>
<header>
<date/time>
The kernel always raises the processor‘s IRQL to DPC/dispatch level or above when it need to synchronize access to shared kernel structures. This disables additional software interrupts and thread dispatching. When the kernel detects that dispatching should occur, it requests a DPC/dispatch level interrupt. But because the IRQL is at or above that level, the processor holds the interrupt in check.
When the kernel completes its current activity, it sees that it‘s going to lower the IRQL below DPC/dispatch level and checks to see whether any dispatch interrupts are pending. If there are, the IRQL drops to DPC/dispatch level and the dispatch interrupts are processed.

## Slide 22: I/O Completion: Asynchronous Procedure Calls (APCs)
Execute code in context of a particular user thread
  APC routines can acquire resources (objects), incur page faults, call system services
APC queue is thread-specific
User mode & kernel mode APCs
  Permission required for user mode APCs
Executive uses APCs to complete work in thread space
  Wait for asynchronous I/O operation
  Emulate delivery of POSIX signals
  Make threads suspend/terminate itself (env. subsystems)
APCs are delivered when thread is in alertable wait state
  WaitForMultipleObjectsEx(), SleepEx()

## Slide 23: Asynchronous Procedure Calls (APCs)
Special kernel APCs
  Run in kernel mode, at IRQL 1
  Always deliverable unless thread is already at IRQL 1 or above
  Used for I/O completion reporting from “arbitrary thread context”
  Kernel-mode interface is linkable, but not documented
“Ordinary” kernel APCs
  Always deliverable if at IRQL 0, unless explicitly disabled (disable with KeEnterCriticalRegion)
User mode APCs
  Used for I/O completion callback routines (see ReadFileEx, WriteFileEx); also, QueueUserApc
  Only deliverable when thread is in “alertable wait”
Thread
Object
K
U
APC objects
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Windows is not a Real-Time OS
Application threads can only run when IRQL is at passive level
  Interrupts, DPC, and APC execution interrupts user-level threads
  Even real-time priority threads will not execute
Ordering of DPCs cannot be controlled by apps.
  A low-priority thread may initiate I/O operations which in turn prevent real-time threads from running
Windows cannot guarantee deterministic response time to external stimuli
  Third-party add-ons (VentureCom, Beckhoff) function as device drivers and may provide real-time behavior

## Slide 25: Real-Time Systems with Windows CE
High-performance embedded applications must often manage time-critical responses.
  manufacturing process controls,
  high-speed data acquisition devices,
  medical monitoring equipment,
  laboratory experiment control,
  automobile engine control,
  robotics systems.
Validating such an application means examining not only its computational accuracy, but also the timeliness of its results.
The application must deliver its responses within specified time parameters in real-time.
Notes: <number>
<footer>
<header>
<date/time>
It is important to distinguish between a real-time system and a real-time operating system (RTOS). The real-time system represents the set of all system elements - the hardware, operating system, and applications - that are needed to meet the system requirements. The RTOS is just one element of the complete real-time system and must provide sufficient functionality to enable the overall real-time system to meet its requirements.
It is also important to distinguish between a fast operating system and an RTOS. Speed, although useful for meeting the overall requirements, does not by itself meet the requirements for an RTOS. The Internet newsgroup comp.realtime lists some requirements that an operating system must meet to be considered an RTOS:
  The OS (operating system) must be multithreaded and preemptive.
  The OS must support thread priority.
  A system of priority inheritance must exist.
  The OS must support predictable thread synchronization mechanisms.

## Slide 26: Windows CE Characteristics
CE kernel design meets the minimum requirements of an RTOS:
  multithreaded and preemptive.
  supports 256 levels of thread priority.
  supports a system of priority inheritance (to correct priority inversion)
  predictable thread synchronization mechanisms,
    including such wait objects as mutex, critical section,
    named and unnamed event objects, which are queued based on thread priority.
    Windows CE supports access to system timers.
Interrupt latency is predictable and bounded.
The time for every system call (KCALL) is predictable and independent of the number of objects in the system.
  The system call time can be validated using the instrumented kernel
Notes: <number>
<footer>
<header>
<date/time>
Windows CE 3.0 presents the most dramatic change with respect to scheduling, resource management, and timing behavior in contrast to earlier versions of Windows CE.
Newer versions of Windows CE have mainly added functionality above the kernel layer, such as better connectivity, support for services such as ftp and http, and support for programming models such as .NET.
Thus, our discussion of Windows CE real-time characteristics is applicable to current versions of Windows CE as well.

## Slide 27: Threads and Thread Priority
Priority level | Constant and Description
0 (highest) | THREAD_PRIORITY_TIME_CRITICAL (highest priority)
1 | THREAD_PRIORITY_HIGHEST
2 | THREAD_PRIORITY_ABOVE_NORMAL
3 | THREAD_PRIORITY_NORMAL
4 | THREAD_PRIORITY_BELOW_NORMAL
5 | THREAD_PRIORITY_LOWEST
6 | THREAD_PRIORITY_ABOVE_IDLE
7 (lowest) | THREAD_PRIORITY_IDLE (lowest priority)
Windows CE 3.0 and later provide 256 priority levels
32 simultaneous processes; one primary thread.
  unspecified number of additional threads.
  actual number of threads is limited only by available system resources.
priority-based time-slice algorithm
  schedule the execution of threads
  eight discrete priority levels, from 0 through 7,
  0 represents the highest priority (header file winbase.h)

## Slide 28: Priority Assignment
Levels 0 and 1: real-time processing and device drivers;
Levels 2-4: kernel threads and normal applications;
Levels 5-7: apps that can always be preempted by other apps.
Preemption is based solely on the thread's priority.
  Threads with a higher priority are scheduled to run first.
  Threads at the same priority level run in a round-robin fashion with each thread receiving a quantum or slice of execution time.
  The quantum has a default value of 25 milliseconds (CE version 3.0 and later supports changes to the quantum value).
  Threads at a lower priority do not run until all threads with a higher priority have finished, that is, until they either yield or are blocked.
  Exception: threads at the highest priority level (level 0) do not share the time slice with other threads at the highest priority level. These threads continue executing until they have finished.
Thread priorities are fixed and do not change.
  Windows CE does not age priorities and does not mask interrupts based on these levels

## Slide 29: Priority Inheritance – circumvent priority inversion problems
Thread priorities are fixed and do not change.
Windows CE does not age priorities and does not mask interrupts based on these levels.
Only kernel modifies priorities temporarily to avoid "priority inversion."
NORMAL
TIME_CRITICAL
Time
TL locks resource
TH starts, request resource
TH continues to completion
TL is boosted until it frees resource
TL runs as scheduled
ABOVE_NORMAL
TM starts
TM runs as scheduled
Priority level

## Slide 30: Thread Synchronization
CE offers a rich set of "wait objects" for thread synchronization.
  critical section, event, and mutex objects.
  wait objects allow a thread to block its own execution and wait until the specified object changes.
Windows CE queues mutex, critical section, and event requests in "FIFO-by-priority" order
  a different FIFO queue is defined for each of the eight discrete priority levels.
  A new request from a thread at a given priority is placed at the end of that priority's list.
  The scheduler adjusts these queues when priority inversions occur.
Windows CE supports standard Windows timer API functions
  Obtain time intervals from the kernel through software interrupts.
  Threads can use the system's interval timer by calling GetTickCount, which returns a count of milliseconds.
  Use QueryPerformanceCounter and QueryPerformanceFrequency for more detailed timing information. (OEM must provide higher-resolution timer and OAL interfaces to the timer.)

## Slide 31: Virtual Memory & Real-Time
Paging I/O occurs at a lower priority level than the real-time priority process levels.
  Paging within the real-time process is still free to occur
  Background virtual memory management won't interfere with processing at real-time priorities.
Real-time threads should be locked into memory to prevent nondeterministic paging delays resulting from VM system.
Windows CE allows memory mapping
  Multiple processes may share the same physical memory.
  Very fast data transfers between processes / driver / app.
  Memory mapping can be used to dramatically enhance real-time performance

## Slide 32: Interrupt Handling: IRQs, ISRs, and ISTs
Windows CE balances performance and ease of implementation by splitting interrupt processing into two steps: an interrupt service routine (ISR) and an interrupt service thread (IST).
Hardware interrupt request lines (IRQ) are associated with ISRs.
  When interrupts are enabled and an interrupt occurs, the kernel calls the registered ISR for that interrupt.
  It is ISR’s responsibility to direct the kernel to launch the appropriate IST.
ISR performs minimal processing and returns an interrupt ID to the kernel.
The kernel examines interrupt ID and sets the associated event.
The interrupt service thread is waiting on that event.
  When the kernel sets the event, the IST starts its additional interrupt processing.
  Most of the interrupt handling actually occurs within the IST.
  The two highest thread priority levels (levels 0 and 1) are usually assigned to ISTs.

## Slide 33: Windows CE Interrupt Architecture - Nested interrupts
Full support for nested interrupts
Based on support by the CPU and/or additional hardware
Nested in order of priority
Kernel will save and restore all required registers

## Slide 34: Interrupt Architecture
ISR runs as part of the kernel
  Multiple interrupt priorities dependent on CPU and available hardware
  Can’t make system calls while in ISR
    No memory allocation, file system access, load module, etc.
IST runs as part of a user mode DLL
  Full access to system services
  Can still access hardware if necessary
  Utilizes normal thread priorities and scheduler
  ISR and IST priorities independent for maximum flexibility

## Slide 35: ISR and IST Model
Interrupt Service Routine
  Typically very short, fast, assembly code
  Job is to return logical Interrupt ID to the Kernel.
  For Example… Serial Interrupt may be identified as SYSINTR_SERIAL
// ISR
// Interrupts are Disabled
Identify the Interrupt, Mask or Dismiss the Interrupt
Return the Interrupt ID
// Interrupts are on again.

## Slide 36: ISR and IST Model
Interrupt Service Thread
  Part of a device driver (DLL)
  Built in or loaded by Device.exe
// Serial Device Driver (IST)
// Setup Hardware
hEvent=CreateEvent( … );
InterruptInitialize(hEvent,SYSINTR_SERIAL);
CreateThread( … );
// ------------------ Thread Code -----------------
While( TRUE ) {
WaitForSingleObject(hEvent,timeout);
{ DoStuff( ); }
InterruptDone(SYSINTR_SERIAL);
}

## Slide 37: Interrupt Block Diagram Drivers for built-in devices
Kernel Components
Device Driver
Interrupt
Service
Thread
PDD
Routines
Interrupt
Service Routine
OAL
Routines
Exception
Handler
Hardware
Interrupt
Support Handler

## Slide 38: Windows CE: Architectural Remarks
Windows CE runs all device drivers inside a user-space process: Devices.exe
  Resembles microkernel architecture
Programmer has full control on priority of Interrupt Service Threads (IST)
  Kernel-mode Interrupt Service Routine (ISR) is short and mainly signals an event to IST
  Windows CE can be configured to run everything in kernel mode (minimize context switching overheads)

## Slide 39: Bounded Interrupt Latency (for threads locked in memory)
ISR latency:
start of ISR = Kernel1 + dISR_Current + sum(dISR_Higher)
  Kernel1 = latency value due to processing within the kernel.
  dISR_Current = duration of ISR in progress at interrupt arrival. (0 .. max( Texec(ISR))).
  sum(dISR_Higher) = sum of the durations of all higher priority ISRs that arrive before this ISR starts; (for interrupts that arrive during the time Kernel1 + dISR_Current)
IST latency:
start of IST = Kernel2 + sum(dIST) + sum(dISR)
  Kernel2 = latency value due to processing within the kernel.
  sum(dIST) = sum of the durations of all higher priority ISTs and thread context switch times that occur between this ISR and its start of IST.
  sum(dISR) = The sum of the durations of all other ISRs that run between this interrupt's ISR and its IST.

## Slide 40: Example
Embedded system with only one critical-priority ISR.
  ISR is set to the highest priority (no higher priority ISRs) -> dISR_Higher = 0.
  latencymin = Kernel1.
  latencymax = Kernel1 plus the duration of the longest ISR.
No other ISTs can intervene between ISR and its IST.
  However, it is possible that other ISRs can be processed between the time-critical ISR and the start of its associated IST.
Pathological case:
  A constant stream of ISRs, postpones the start of IST indefinitely.
  Unlikely, OEM has control over the number of interrupts in the system.
To minimize latency times, the OEM can control the processing times of the ISR and IST, interrupt priorities, and thread priorities.

## Slide 41: Validating the Real-time Performance of Windows CE
In-house inspection and analysis of the kernel code by the Windows CE development team, and
OEM and ISV (independent software vendor) timing validation of specific configurations using tools that will be provided in future versions of the Windows CE Embedded Toolkit for Visual C++.
The Windows CE Embedded Toolkit for Visual C++ includes:
An instrumented version of the kernel for timing studies, and
The Intrtime.exe utility for observing minimum, maximum, and average time to interrupt processing.

## Slide 42: Performance Tools
Provided in Platform Builder to measure real-time performance of your system
  ISR/IST Latency
  Scheduling performance
Event logging tool useful for debugging and performance tuning
More information on these tools available in the Platform Builder Online Help

## Slide 43: Measurements – varying number of system objects
Start of ISR times are independent of #system objects
Start of ISRMax | Numbers of background threads (with one event per thread) | Background thread priority
8.4 S | 0 | 7
8.6 S | 5 (Note: represents only 100 tests) | 7
9.0 S | 10 (Note: represents only 100 tests) | 5
14.8 S | 10 | 5
19.2 S | 10 | 5
17.0 S | 10 | 7
12.8 S | 20 | 5
11.0 S | 20 (Note: represents only 100 tests) | 7
10.0 S | 50 | 7
15.0 S | 100 | 5
15.6 S | 100 | 7

## Slide 44: Windows CE Has Deterministic Performance!
ILTiming and OSBench tools running on development versions show that latencies are bounded
For a Pentium 166 MHz class system (Remember: embedded systems are small and with limited resources - CPU, Memory, Power)
  ISR < 10 S
  IST < 100 S

## Slide 45: Getting Real-Time Performance
Don’t:
  Spend inordinate amounts of time in ISRs
  Spin in your highest priority thread, you’ll starve the system
  Use APIs that are not real-time and expect real-time performance
    SetTimer, file system calls, process or thread creation,…
  Allow priority inversions to occur

## Slide 46: Getting Real-Time Performance
Do:
  Pre-allocate all your resources
    Memory, threads, processes, mutexes, semaphores, events, etc…
  Buffer data in ISR if passing it directly to the IST isn’t fast enough
  Use ISR to do all work if…
    …No system services are required
    …No extensive processing (long ISR time) required
  Set priorities and quantums correctly
  Use LoadDriver() to instead of LoadLibrary() to avoid page faults
    Or turn the demand-pager off

## Slide 47: References
msdn.microsoft.com/embedded/usewinemb/ce/techno/realtme/default.aspx
http://msdn.microsoft.com/library/default.asp?url=/library/en-us/dnanchor/html/windowsce.asp
http://msdn.microsoft.com/library/default.asp?url=/library/en-us/wcemain4/html/cmconreal-timeperformancefunctionality.asp

## Slide 48: Further Reading
Douglas Boling, Programming Microsoft Windows CE .NET, Third Edition, MS Press, 2003
Mark E. Russinovich and David A. Solomon, Microsoft Windows Internals, 4th Edition, Microsoft Press, 2004.
  Chapter 3- System Mechanisms (from pp. 85)
  p.102 - box on "Windows and Real-Time Processing
msdn.microsoft.com/embedded/windowsce/default.aspx